## Slide 1: HDMI Transmitter
Suraj Khan

## Slide 2
HDMI or High Definition Multimedia interface is actually protocol which allows to transmit video as well as audio data
The protocol consists of two main system architectures
  Source
  Sink
Became an IEEE official standard in 2003.
Introduction

## Slide 3: Introduction
HDMI specs until version 2.0
  Encoding Scheme : TMDS – Transition Minimized Differential Signaling (8b/10b scheme)
  Max Data Rate : upto 18 Gbps
  Data Channels: 3
  Supported Colour Bits: from 8 Bit per channel all the way to 16 bits per channel
  Audio specifications: Max Sampling Rate: 192 KHz with support for upto 32 channels with each sample size from 16 to 32 bits.

## Slide 4: Goals for this project
Build a simple HDMI transmitter which outputs a simple image of resolution of 640 x 480
Implement the system on the Verilog
Use the hardware to display an output of your choice on the monitor

## Slide 5: Overview of the Transmitter System

## Slide 6: Overview of the Transmitter System

## Slide 7: HDMI Pins layout
Notes: 2+,2-,1+,1-,clk+,clk-

## Slide 8: Overview of the Video Signals
The video signals have two main phases
  Blanking Intervals
  Active Pixels or the actual image draw area
Blanking intervals contain the sync data as well as can also carry audio data

## Slide 9
640px
16px
96px
48px
800px
480px
10px
2px
33px
525px
640x480px

## Slide 10: Timing specifications for 640x480
Aspect Ratio 4:3
Pixel Clock 25.175 MHz , TMDS Clock 251.750 MHz , Pixel Time 39.7 ns ±0.5%
Frame Time 16.7 ms
Horizontal Timings
  Active Pixels 640
  Front Porch 16 , Sync Width 96, Back Porch 48 Blanking Total 160
  Total Pixels 800
Vertical Timings
  Active Lines 480
  Front Porch 10 , Sync Width 2 ,Back Porch 33 , Blanking Total 45
  Total Lines 525
Active Pixels 307,200 and Data Rate: 0.60 Gbps

## Slide 11: Overall Verilog Blocks
Clock Generator
Pix_clk
HDMI
Pixel
Output Logic
TMDS
Encoding
8b/10b
&
Serializer
sysclk
TMDS
clk
sync
VDE
TMDS R
TMDS G
TMDS B
TMDS PixClk
Your Task for the Lab
Offered to you

## Slide 12: Clocking Generator
Inbuilt FPGA clock: 125 MHz
Required clocking signals:
  25 MHz for pixel clock
  250 MHz for TMDS clock
Techniques for generating two clocks from same clock?
  CMT - Clock Management Tiles
    Each CMT contains MMCM – Mixed Mode Clock generator and PLL (Phase Locked Loop)
Advantages of MMCM over PLL
  Fractional Multiplication and Divide as compared to PLL
  Fine phase shifting as well as Dynamic Phase Shifting
  Inverted Clock Outputs

## Slide 13: MMCM Instances in series 7 FPGAs
First instantiate the base MMCM parameters

## Slide 14: MMCM Instances in series 7 FPGAs

## Slide 15: Instantiate the actual clock

## Slide 16: Additional Global Buffers
Global buffers are essential for clocks signals to keep stability
Preferable to have a global buffer for each divided clock output
Ideal to also include a buffer for feedback clock for the MMCM module to keep the phase locked.

## Slide 17: TMDS Signalling
The TMDS Encoder contains of two parts
  Transition Minimizing. If number of transitions in the 8bit signal is greater than 4 apply XOR or else XNOR. 9th Bit indicates if XOR is used.
  DC balancing: The number of ones and zeros in the 10 bits should be equal. So the 10th bit is decided accordingly.

## Slide 18: TMDS Encoding Algorithm

## Slide 19: HDMI Sync Signals
Hsync and Vsync signals on the blue channel
  Hsync signal is high for 96 pixels for pixels starting from 656 till 751(inclusive) horizontal pixel.
  Vsync signal is high for signals for vertical pixel 490 to 491 (inclusive)
For red and green channels send 2 bit zeros as sync signals
Red and Green channels carries HDCP and other control signals, not required in this case of lab.

## Slide 20: Interfacing on the board
Use constraints to connect your Verilog logic to the ports on the board
  Use appropriate constraint to connect to the 125 MHz crystal clock output for the FPGA
  Define appropriate constraints to connect to the TMDS Red, Green and Blue and clock lines on the HDMI output connector
  Select 3V3 as the output signalling for the HDMI TMDS connection

## Slide 21: Goals for this Lab
Building the appropriate clock generator for Pixel and TMDS clocks
Build the HDMI color generation logic
Apply constraints to connect to appropriate ports on the board

## Slide 22: Summary
Specs
HDMI transmitter
Resolution : 640x480
Two clocks: Pixel and TMDS clock of 25MHz and 125 MHz respectively
Ports
sys_clk: 125 MHz system clock
HDMI TMDS for Red, Blue, Green and Clock channel.